## Slide 1: FUFO Project
Final Report

## Slide 2: Contents
Introduction
1
Hardware & Software
2
Algorithms
3
Experiments and results
4
Conclusion
5

## Slide 3: FUFO team
Introduction
PhongVM
ThangVD
NguyenLK
HungHD
YenTT
HungPD Supervisor

## Slide 4: Project Plan
Introduction

## Slide 5: Project Plan
Introduction

## Slide 6: History
Definition:
  A Vertical Take-Off and Landing aircraft.
  Has 4 rotors.
Introduction

## Slide 7: History
The first Quadrocopter was developed in 1920.
No commercialized Quadrocopter because of limitation of technology and science at that time.
Introduction

## Slide 8: History
8 years before 2012, many institutes and companies began to research on this platform as a small UAV.
Introduction

## Slide 9: Commercialized product
Airbot X600-BKPP (€ 34,500)
  Radio control unit (2.4 GHz)
  Live video stream
  GPS waypoint navigation
CyberQuad Maxi ($ 36,000)
  Radio control unit
  GPS waypoint navigation
  Live video stream
Introduction

## Slide 10: Idea
  Develop a Quadrocopter for observation purpose.
Introduction

## Slide 11: Idea
 | Quadrocopter | Helicopter | Fixed-Wing aircraft
Aerodynamics mechanical design | Medium | Complicated | Complicated
Control method | Medium | Medium | Complicated
Runway | No | No | Yes
 Quadrocopter is more suitable for embedded Engineering students who are not familiar with aerospace issue and mechanical design.
Introduction
Why choosing Quadrocopter platform?

## Slide 12: Idea
 | Android phone | In-circuit designs
Software development | Android SDK | Linux, C30…
Evaluation of controlling by phone/tablet via Bluetooth? | Yes | No
Risk and complexity in hardware design | Low | High
Cost | Low | High
Has built-in camera, Wi-Fi, 3G module
Phone is still usable after this Capstone project
Introduction
Why choosing Android Phone?

## Slide 13: Idea
Sensor data
Command
Bluetooth
Introduction

## Slide 14: Idea
Picture
JPEG
Picture
JPEG
Introduction

## Slide 15: Idea
Control Mode
Autonomous(Dynamic Stabilization)
Manual
Introduction

## Slide 16: Idea
Manual mode
Wind
Introduction

## Slide 17: Idea
Go to 1m
Wind
Dynamic stabilization
SAFE
Dynamic Stablization
Introduction

## Slide 18: Hardware study
Hard & Soft
No. | Components | Quantity | Description
1 | dsPIC30f4012 | 1 | Microcontroller
2 | HC-06 | 1 | Bluetooth module
3 | BMP085 | 1 | Barometer
4 | L3G4200D | 1 | Gyroscope
5 | ADXL345 | 1 | Accelerometer
6 | HW 30A ESC | 4 | Electronic speed Controller
7 | Himodel 2212 1400kv | 4 | Brushless motor
8 | Turnigy 3000mAh 11.1v 3s | 2 | Li-Po battery pack.
9 | HTC HD2 | 1 | Android 2.3 phone

## Slide 19: Hardware study
Hard & Soft
dsPIC30f4012 Microcontroller
  Max speed: 30 MIPS
  16x16 bit working arrays
  5 timers, 3 PWM generators
  Programmable by C30.

## Slide 20: Hardware study
Hard & Soft
BMP085 + ADX345 + L3G4200D
  All-in-one module:
    3-axis accelerometer.
    3-axis gyroscope.
    -300m to 9000m altimeter.

## Slide 21: Hardware study
Hard & Soft
Turnigy 3000mAh battery pack
  3000mAh x 2
  253 grams x 2
  11.1v
  Discharge rate: 20C

## Slide 22: Hardware study
Hard & Soft
Motor and ESC
  1400kv Brushless motors
  8x4” propellers
  ESC PWM range: 1ms – 2ms

## Slide 23: Hardware study
Hard & Soft
HTC HD2 Android 2.3
  320x240 camera.
  Has Bluetooth and Wi-Fi connection
  Run on Android 2.3

## Slide 24: Hardware design
Hard & Soft

## Slide 25: Hardware design
Hard & Soft

## Slide 26: Frame design
Hard & Soft
Motor mount
Circuit mount
440 mm
Fiber Glass & Fiber Carbon

## Slide 27: FUFO Quadrocopter
Hard & Soft

## Slide 28: Software study
Hard & Soft
Iterative model:

## Slide 29: Software study
Hard & Soft
Embedded system development:

## Slide 30: Software study
Hard & Soft
Three software:
  Software on PC
  Software on Phone
  Firmware

## Slide 31: Software study
Hard & Soft
FSM:
Start
WaitingForConnection
Verify
Pending
SetupForFlight
Ready
Hovering
Landing
Error
Power on
System initiated
System connected
Control
method
selected
Start button
pressed
Sensor data
initiated
First altitude
is chosen
Any error
Altitude is
set to zero
Motor stopped

## Slide 32: Software study
Hard & Soft
PC interface:

## Slide 33: Software study
Hard & Soft
Android interface:

## Slide 34: Quadrocopter Dynamic
Algorithms
Inertial Frame, Body frame and Euler Angle:

## Slide 35: Quadrocopter Dynamic
Algorithms
Input:
  𝜂1 = [x,y,z];
  𝜂2 = [𝜃,𝜑,𝜓];
  x = y = 0.
Output:
  [F1,F2,F3,F4]
  Linear translational movement
  Rotational movement

## Slide 36: PID Control system
Algorithms
Open-loop feedback controller:

## Slide 37: Signal Processing
Algorithms
Euler angles calculation:
  Gyroscope: Integration of angular velocity over time.
  Accelerometer: Multiplication with a (x,y,z) Direction Cosine Transformation Matrix.

## Slide 38: Signal Processing
Algorithms
Theta angle by Accelerometer and Gyroscope:
BEFORE FILTER
AFTER HIGH-PASS AND LOW-PASS FILTER

## Slide 39: Signal Processing
Algorithms
Theta angle by Accelerometer and Gyroscope:
AFTER COMPLEMENTARY FILTER

## Slide 40: Result
Experiment
Test
Strategy

## Slide 41: Result
 | Project | FUFO | Start-Date | 28-Jul | Evaluation | OK
 | Buglist ST |  | End-Date | 20-Aug |  | 
 | No | Module Name | Number of bugs | Number of bug Fixed | Module status | Note
 | 1 | AOC | 7 | 7 | OK | 
 | 2 | FUFO | 3 | 3 | OK | 
 | 3 | AOP | 6 | 6 | OK | 
Experiment
Chart: 
| AOC | FUFO | AOP
 | 7 | 2 | 8
Function | Unit test |  |  |  | Unit test |  |  |  | 
 | Test case |  | Bug |  | Test case |  | Bug |  | Result
 | Plan | Actual | Plan | Actual | Plan | Actual | Plan | Actual | 
AOC | 65 | 63 | 7 | 8 | 55 | 53 | 6 | 6 | OK
FUFO | 30 | 27 | 3 | 2 | 25 | 27 | 2 | 3 | OK
AOP | 60 | 62 | 6 | 8 | 50 | 57 | 5 | 5 | OK

## Slide 42: Results
Experiment
Indoor flight:

## Slide 43: Results
Experiment
Outdoor flight:

## Slide 44: Achievement
Conclusion
Successfully proved the correctness of the aforementioned algorithms.
Understand more about this flying platform for further improvement and development.

## Slide 45: Future Improvement
Conclusion
Develop a higher response system.
Hold altitude in narrow and low area with precision of +-0.1 m
Hold a specified position on map or moving on a track.
Obstacle detection and avoidance.
CMOS camera's video transmission over long distance.
Object detection based on image processing.

## Slide 46
www.themegallery.com
Thank You !
From FUFO team with love