## Slide 1: FUFO overview
Confidential document

## Slide 2: Contents
Idea
1
Overview
2
Scope
3
Detail
4

## Slide 3: The needs
The need of security observation from above. E.g.:
  Olympic Game Events.
  Independence Day Event.
  Protection Activities of Government’s important guest.
Daily protection of the Nation boundary. E.g.:
  Cross-border smuggling control.
  Detect maritime boundary violation early.
Idea

## Slide 4: The facts
 | Static Cam | Human patrol | Air plane | UAV
Cost | Low | Medium | Ultra High | Ultra High
Mobilization | No | Yes | Yes | Yes
Speed | N/A | Low | High | High
Safety critical | No | Yes | Yes | No
Terrain barrier | Yes | Yes | No | No
=> The modern solution should be Unmanned Aerial Vehicle (UAV) but in a cheaper price.
Idea

## Slide 5: The facts
 | RC UAV | Military UAV
Flight Time | Short | Long
Size | Small | Big
Cost | Low | Ultra High
Infrastructure needed | Low | Ultra High
Reliability | Low | High
Mass production | Possible | Impossible
              VS
Idea

## Slide 6: The future
Next generation batteries (graphene, nano, themor, solar..)
Increase Flight time and reliability of RC UAV
The development of 3G, Municipal Wi-Fi, satellite..
Near future
Idea

## Slide 7: The innovation
FUFO
Next generation energy
RC UAV Quadrocopter
3G, Municipal wifi infrastructure
Idea

## Slide 8: FUFO Overview
Project name: FUFO
Project type: Research and Development
Project purpose: Develop a commercialized Quadrocopter.
Base on observation on the similar projects, a project this big may need four phases, each phase will be a relevant project to lead to the final product.
  <More detailed requirement information will be specify in the next slide>
Overview

## Slide 9: FUFO Overview
FUFO phases:
  Evaluation Phase
  Development Phase
  Optimization Phase
  Commercial Phase
Our FPT University Capstone project just focuses on the first phase of FUFO project.
  <More detailed requirement information will be specify in the next slide>
Overview
Capstone project

## Slide 10: FUFO Overview
No. | Name | Estimated duration (Month) | Success criteria
1 | Evaluation phase (Capstone Project) | 4 | Evaluation report and a Quadrocopter with basic functions that might meet customer needs.
2 | Development phase | 12 | A system whose functional requirements meet customer needs.
3 | Optimization phase | 12 | A system whose functional and non-functional requirement meet customer needs.
4 | Commercial phase | 12 | A system that are able to be mass-produced.
Evaluation
(Capstone project)
Development
Optimization
Commercial
Overview

## Slide 11: Why Quadrocopter?
 | Quadrocopter | Helicopter | Fixed-Wing aircraft
Aerodynamics mechanical design | No | Yes | Yes
Control method | Medium | Medium | Complicated
Runway | No | No | Yes
=> Quadrocopter is more suitable for Computer Engineering students who are not familiar with aerodynamic issue and mechanical design.
Overview

## Slide 12: Why Android Phone?
Overview
 | Android phone | In-circuit designs
Software development | Android SDK | Linux, C30…
Evaluation of controlling by phone/tablet via Bluetooth? | Yes | No
Risk and complexity in hardware design | Low | High
Cost | Low | High
Has built-in camera, Wi-Fi, 3G module
Phone is still usable after this Capstone project

## Slide 13: Capstone project’s aim
The aims of this Capstone project are:
  Make a simple Quadrocopter.
  Use Bluetooth protocol to communicate an Android Smart Phone with the Quadrocopter.
  Use Internet Protocol to communicate a PC with Android Smart Phone.
  Make two study report:
    Study report on hovering capability of Quadrocopter.
    Study report on real-time video transmission.
Scope

## Slide 14: Quadrocopter
Quadrocopter:
  Max speed < 60 km/h under “good condition”(*)
  Can hover and keep stable in “light wind” (**)
  Under good condition can capture stable video stream.
  Can carry >500 grams and hover >30m high.
  Batteries last ~15 minutes without carrying anything
  (*) good condition is a condition where wind speed ~ 0m/s, temperature 10 - 30 Celsius, acceptable humidity.
  (**) what is “light wind” will be investigated during the project time.
Scope

## Slide 15: Quadrocopter
Scope

## Slide 16: Communication
Communication:
  Communicate via Bluetooth:
    Quadrocopter sends Sensor data (angle rate, acceleration rate..) to Android Smart Phone.
    Android Smart Phone sends Control commands to Quadrocopter.
  Communicate via Internet Protocol:
    PC sends Control command to Android Smart Phone
    Android Smart Phone sends Real-time video (no sound) and Quadrocopter Sensor data to PC.
Scope

## Slide 17: Communication
Sensor data
Command
Bluetooth
Scope

## Slide 18: Real-time video
Real-time video transmission:
  Protocol: UDP/IP.
  Latency < 0.5 seconds
  FPS ~ 10
  No sound
  Images are compressed into JPEG.
Scope

## Slide 19: Real-time video
Picture
JPEG
Picture
JPEG
Scope

## Slide 20: Control
Control:
  The Quadrocopter has two control mode:
    Autonomous
    Manual
  Autonomous mode:
    Dynamic stabilization.
  Manual mode:
    Pilot can control the Quadrocopter with little effort.
Scope

## Slide 21: Control
Control Mode
Autonomous(Dynamic Stabilization)
Manual
Scope

## Slide 22: Control
Manual mode
Wind
Scope

## Slide 23: Control
Manual mode
Wind
Enter Autonomous mode
SAFE
Dynamic Stablization
Scope

## Slide 24: Comparation
 | FUFO Quadrocopter v1.x | Comercialized Quadrocopter
Carrying capacity | 500gr | Vary
3G network | Yes | No
Wifi network | Yes | No
Bluetooth | Yes | Maybe
RF | No | Yes
Real-time video | Yes | Optional
Dynamic stability | Yes | Yes
Controller | PC & Smart Phone | RF Controller
Auto-pilot | No | Maybe
Scope

## Slide 25: PC application
PC application:
  Receives video and Sensor’s statuses from Android Smart Phone and display them.
  Sends control command to Android Smart Phone.
  Easy to use and good looking.
  Easy to maintain and update.
Detail

## Slide 26: Android application
Android application:
  Receives control command from PC.
  Sends control command to Quadrocopter.
  Send video and Sensor’s statuses to PC. Easy to use.
  Easy to maintain and update.
Detail

## Slide 27: Embedded Software
Embedded Software:
  Receive control command from Android Smart Phone and control the motors.
  Send Sensor’s output to Android Smart Phone at a desirable rate.
  Go into Autonomous Mode when no control command is received from pilot.
  Use Bluetooth RS232 communication method to communicate with Android Smart Phone.
  Easy to maintain and update.
Detail

## Slide 28: Embedded Hardware
Embedded Hardware:
  Build a Quadrocopter frame which has space for a 150gr Smart Phone.
  Design a PCB board for controlling the Quadrocopter, it should has:
    Bluetooth module.
    At least 4 PWM generators
    Tri-angle Accelerometer and Gyroscope sensors.
  Motors, ESCs, Batteries can be bought from the market.
    Motor’s thrust > 800gr
    Batteries: 4400mAh
Detail

## Slide 29
www.themegallery.com
Thank You !
Confidential document